## Slide 1
Source Apportionment Techniques Conventional and Real-Time Approaches
Definitions, core principles, model differences, and practical workflows for PCA, CMB, PMF, and real-time systems.
Manos Manousakas, NCSR Demokritos
Teaching presentation
What the presentation covers
What source apportionment (SA) means and how it works
The main conventional receptor-model techniques: PCA, CMB, and PMF
Key differences between the techniques and what each method can and cannot say
How near-real-time / real-time SA can be implemented using online measurements
Conventional SA
Model comparison
Real-time SA

## Slide 2
1. What is source apportionment?
Goal: identify the sources of particulate matter and quantify how much each source contributes.
Source apportionment (SA) is the practice of deriving information about pollution sources from ambient air-quality data.
For particulate matter (PM), SA usually aims to answer two questions:
  Which sources are present?
  How much does each source contribute over time?
The output is usually a set of source profiles (chemical fingerprints) and source contributions (time series or average mass contributions).
SA results are used to support air-quality management, evaluate control measures, and interpret pollution episodes.
Basic idea
Traffic EC, Cu, Zn
Biomass burning K, BC, OC
Dust / soil Al, Si, Ca, Fe
Ambient PM measurements chemical species × time
Different sources leave different chemical fingerprints in the ambient aerosol. SA exploits these fingerprints.

## Slide 3
2. How does source apportionment work?
Most SA methods are based on measured PM composition and mass-balance ideas.
Measured data matrix X (samples × species)
=
Source contributions G (samples × factors)
×
Source profiles F (factors × species)
+
Residuals E
The model tries to explain the measured concentrations as the sum of multiple source contributions.
A “profile” describes which species characterize a source; a “contribution” describes how strong that source is at each time point.
Different methods solve the problem in different ways depending on what prior information is available.
Typical information used: elemental composition, ions, EC/OC, black carbon, organics, and total PM mass.

## Slide 4
3. Conventional versus real-time SA
The basic scientific objective is the same; the main differences are data latency, time resolution, and automation.
Conventional / offline SA
Real-time / near-real-time SA
Filter sampling followed by laboratory analysis.
Time resolution often 24 h (sometimes higher or lower).
Analyst usually has time to test multiple model runs and validate the final solution carefully.
Strong for robust long-term datasets and detailed interpretation, but results are delayed.
Online instruments measure PM components continuously.
Time resolution can be hourly, sub-hourly, or even minutes.
Automated software can update source contributions almost immediately after measurement.
Strong for episode tracking, diurnal patterns, and timely action, but depends on stable setup and good prior optimization.
Sampling
Lab analysis
Modeling
Results
Measure
Auto-QC
Auto-model
Updated SA

## Slide 5
4. The model landscape
In practice, SA combines statistics, atmospheric understanding, and supporting measurements.
Source apportionment methods include receptor models, source-oriented models, chemical reconstruction, and hybrid approaches.
Receptor models focus on the composition measured at the receptor site.
Source-oriented models (e.g., chemical transport models) simulate emissions, transport, chemistry, and deposition.
This presentation focuses on the main conventional receptor-model techniques: PCA, CMB, and PMF.
Exploratory statistics PCA / FA
Known source profiles CMB
Unknown source profiles PMF / ME-2
Automated implementation Real-time SA
No single model is universally “best”. The appropriate method depends on the study question, data quality, and available prior information.

## Slide 6
5. Conventional receptor models
They start from measured ambient composition at the receptor site.
PCA Pattern finder
CMB Known profiles
PMF Unknown profiles
Explores variance and correlations
Uses measured source fingerprints
Finds profiles and contributions together
No model is universally best. Choose based on data, site, and question.

## Slide 7
6. PCA: what it says and how it works
Principal Component Analysis is mainly an exploratory technique for identifying patterns in multivariate data.
What PCA says
PCA transforms a set of correlated variables into a smaller set of uncorrelated principal components (PCs).
Each PC captures a portion of the total variance in the dataset.
In source apportionment, the loadings may suggest source patterns (e.g., a traffic-related component or a crustal component).
By itself, PCA does not directly provide physically constrained source contributions.
How PCA works
Data matrix (samples × species)
PC1 PC2 PC3...
Mathematically, PCA finds new axes in the data space that maximize explained variance, under the constraint that the components are orthogonal.
Strengths Simple, fast, useful for screening
Limitations No uncertainty weighting; negative values possible; interpretation can be ambiguous

## Slide 8
7. PCA: pattern finder
What it does
Compresses many variables
Finds common patterns
Useful first look at the data
New axes = principal components
Important: PCA suggests patterns, but does not directly give physically constrained source contributions.

## Slide 9
8. CMB: what it says and how it works
Chemical Mass Balance estimates source contributions when source profiles are already known.
CMB uses the measured ambient composition together with known source profiles collected from emission sources or from the literature.
The model solves a weighted mass-balance equation to estimate the contribution of each source to each sample.
CMB is powerful when the relevant source list is known and representative source profiles are available.
It becomes difficult when source profiles are missing, mixed, or highly collinear.
Known source profiles
Ambient composition
CMB solver
Source contributions
Good for well-characterized areas
Needs reliable source profiles

## Slide 10
9. PMF: what it says and how it works
Positive Matrix Factorization derives both source profiles and source contributions from the ambient dataset.
PMF solves X = GF + E by minimizing a weighted objective function, usually written as Q = Σ(eij / uij)².
Each data point is weighted by its uncertainty, and non-negativity constraints are imposed on source profiles and contributions.
Unlike CMB, PMF does not require complete source profiles a priori.
The analyst still needs to choose the number of factors and interpret the resulting profiles, contributions, and diagnostics.
X measured data
=
G contrib.
×
F profiles
Weighted least squares + non-negativity + uncertainty information
Strengths widely used, handles uncertainty, no full prior profiles required
Limitations rotational ambiguity, factor mixing, interpretation remains partly subjective

## Slide 11
10. PCA, CMB, and PMF: key differences
A compact comparison of the three conventional techniques.
Criterion | PCA | CMB | PMF
Main purpose | Explore patterns / components | Quantify contributions using known profiles | Resolve factors and contributions from ambient data
Need source profiles? | No | Yes – essential | Not full profiles; can use constraints
Uses uncertainties? | Usually no | Yes | Yes – central to the method
Negative values possible? | Yes | Possible depending on solution | No, non-negative factors/contributions
Main strength | Fast exploratory overview | Direct quantitative apportionment when profiles are known | Flexible and widely applicable
Main limitation | Interpretation can be ambiguous | Depends on accurate source profiles and source list | Needs careful diagnostics and factor interpretation
In practice, PCA is often exploratory, CMB is profile-driven, and PMF is the most commonly used unconstrained receptor model for conventional PM source apportionment.

## Slide 12
11. A practical workflow for conventional SA
Typical steps from study design to interpretation.
1. Study design Select site(s), species, and sampling frequency
2. Measure Collect PM mass and chemical composition
3. Prepare data QA/QC, uncertainties, missing and BDL values
4. Run model PCA / CMB / PMF / ME-2
5. Interpret Assign sources and check diagnostics
Good SA begins before modeling: species selection, temporal coverage, and uncertainty estimation strongly affect the final solution.
The final interpretation should be supported by time series, tracer species, wind/trajectory analysis, and knowledge of local emissions.

## Slide 13
12. What data quality and diagnostics matter most?
Conventional SA is only as good as the input data and the interpretation strategy.
Species selection: choose variables that are informative, stable, and above detection limits often enough.
Uncertainties: estimate them carefully; PMF and CMB explicitly depend on them.
Missing and below-detection-limit values must be treated consistently.
Temporal coverage: enough samples are needed to represent source variability.
External validation: wind direction, trajectories, day-of-week patterns, and independent tracers help validate the solution.
Before modeling scatter plots, time series, ion balance, correlations
During modeling Q values, residuals, factor stability, bootstrap / displacement tests
After modeling source tracers, expected ratios, seasonality, external evidence
Especially for PMF, factor assignment is usually the most subjective step.

## Slide 14
13. Why move toward real-time source apportionment?
Online measurements overcome the latency of offline analysis and reveal fast temporal dynamics.
Traditional offline SA provides valuable results, but often only after sampling, laboratory analysis, and repeated model runs.
Online measurements enable high-time-resolution composition data, which reveal diurnal cycles, short-lived events, and rapid source changes.
Real-time SA can provide updated source contributions within minutes to hours after measurement, supporting faster interpretation and action.
This is especially useful for episodic events such as traffic peaks, dust intrusions, solid-fuel combustion, and industrial plumes.
Latency comparison
Offline
Sample
Lab
Model
Result
days to weeks
Real-time
Measure
Auto-QC
Auto-SA
Update
minutes to hours
Important caveat Real-time systems usually depend on prior optimization and robust quality control.

## Slide 15
14. The instruments behind real-time SA
No single instrument measures all PM components, so multi-instrument setups are used.
ACSM organics + major inorganic ions
Xact / XRF trace elements
Aethalometer black carbon and BC source indicators
AXA setup complementary, high-time-resolution input data
Real-time SA software pre-processing + instrument-specific SA + combined source output
The ACSM–Xact–Aethalometer (AXA) setup is highlighted in the uploaded EAC 2025 and AMT 2025 materials as a practical framework for near-real-time SA.

## Slide 16
15. How can real-time source apportionment work?
A practical implementation often follows a three-step workflow.
Step 1 Measure and process Online instruments provide composition data and standard processed concentrations.
Step 2 Instrument-specific SA Separate automated models estimate source contributions from organics, elements, and black carbon.
Step 3 Recombine results Outputs are merged into complete PM source contributions and updated continuously.
In practice, the model parameters are usually initialized from optimized offline / supervised SA runs and then applied automatically to incoming data.

## Slide 17
16. Real-time model logic and implementation choices
Automation is possible, but the model still needs carefully defined rules.
Real-time SA often uses constrained or semi-constrained models so that known source profiles remain stable.
Moving-window implementations can allow the latest data to be assimilated while preserving model robustness.
Instrument-specific source profiles may be combined after separate real-time runs, or hybrid strategies can be used.
Automatic QA/QC, backups, and alerting are important because the system runs continuously.
Inputs: hourly/sub-hourly data, uncertainty estimates, QC flags
Model engine: PMF / ME-2 / constrained real-time routines
Outputs: updated source time series, dashboards, alerts
Key idea: conventional SA is used to optimize the configuration; real-time SA then applies it automatically.

## Slide 18
17. What does real-time SA add scientifically?
Beyond speed, it improves insight into source dynamics and short-lived events.
Diurnal source patterns become much clearer than in daily offline datasets.
Specific episodes (dust storms, traffic rush hours, fireworks, solid-fuel peaks, industrial plumes) can be isolated in time.
The approach supports operational air-quality management because source-resolved information becomes available quickly.
Recent case studies show strong agreement between real-time results and optimized reference SA when the system is properly configured.
Examples highlighted in the uploaded material
Athens case study: first implementation of the AXA setup with SoFi RT https://doi.org/10.5194/amt-18-3983-2025
Six Chinese cities: strong correlation between near-real-time and optimized source apportionment results
https://doi.org/10.1038/s41598-026-38154-x
Applications emphasize urban air-quality management and timely mitigation.

## Slide 19
18. Conventional versus real-time SA: when should each be used?
The best strategy is often to combine them rather than treat them as competitors.
Question | Conventional SA | Real-time SA
Best for... | robust retrospective analysis, method development, detailed validation | operational monitoring, short events, rapid source-resolved updates
Time resolution | usually daily or multi-hour | hourly to minute-scale
Human involvement | high during data preparation and interpretation | high during setup, lower during routine operation
Main challenge | latency and limited time resolution | instrument stability, automated QA/QC, maintaining valid constraints
Best overall use | optimize and validate the source-apportionment framework | deploy the optimized framework continuously

## Slide 20
19. Take-home messages
A short summary of the main points.
Source apportionment identifies and quantifies PM sources using measured composition data and mass-balance concepts.
PCA is mainly exploratory, CMB is profile-driven, and PMF is the most widely used uncertainty-weighted receptor model for conventional SA.
Conventional SA remains essential for robust interpretation and for defining model settings and source profiles.
Real-time SA uses online measurements and automated workflows to provide source-resolved information within minutes to hours.
In practice, conventional and real-time SA are complementary: optimize first, then automate and deploy.
Best teaching message: understand the assumptions of each model before interpreting the output.