## Slide 1
Long-range transport
methods for PM
Trajectory statistical methods with emphasis on CPF/PSCF and CWT
Part I
Concepts and methods
Part II
HYSPLIT + openair practical workflow
CWT
CPF / PSCF
HYSPLIT
openair
01

## Slide 2
Course roadmap
A practical path from air-mass history to CWT/CPF maps and reproducible R workflows.
Why transport?
Transboundary PM and natural dust
Trajectory data
HYSPLIT endpoints linked to PM
CPF / PSCF + CWT
Probability and weighted concentration maps
Practical tools
Install, import, plot, interpret
Learning outcome
• Explain what a CPF/PSCF map and a CWT map show.
• Choose reasonable trajectory settings and input pollutants.
• Run the core openair commands for trajectory plotting, CPF/PSCF, CWT and clustering.
02

## Slide 3
Why study long-range transport?
Local concentrations may include material transported over hundreds or thousands of kilometres.
Local emissions
traffic • heating • industry
Regional formation
secondary sulfate/nitrate/organic aerosol
Natural transport
African dust • sea salt • wildfire smoke
Receptor site
measured PM = local + regional + long-range contributions
Key message: a decrease in local emissions does not always lead to a proportional decrease in measured PM if transported aerosols or precursors are important.
03

## Slide 4
Air-mass history: the core idea
Back trajectories estimate where the arriving air parcel has travelled before reaching the receptor.
Start at receptor
(time, location, height)
Run backward
24–120 h or longer
Get endpoints
lat • lon • height • time
Back trajectories are estimates, not exact paths. Interpret many trajectories together, not just one.
04

## Slide 5
What does a trajectory model need?
HYSPLIT and similar models use gridded meteorology to calculate air-mass paths.
Receptor
latitude / longitude
Arrival time
UTC date + hour
Starting height
AGL / ASL
Run duration
backward hours
Meteorology
GDAS / GFS / other
Output: a table of trajectory endpoints
date
date2
hour.inc
lat
lon
height
pressure
These endpoints can be joined with pollutant concentrations measured at the arrival time.
05

## Slide 6
Why trajectory statistical methods?
A single back trajectory is useful for context, but it is not enough for source-region identification.
Single trajectory
• uncertain path
• sensitive to height and meteorology
• cannot prove source–receptor link
Large trajectory ensemble
• hundreds to thousands of endpoints
• uncertainty partly averages out
• patterns become visible
TSM result
• transport pathways
• potential source regions
• meteorological regimes
Trajectory statistical methods combine many trajectories with measured pollutant concentrations.
06

## Slide 7
Trajectory statistical methods: workflow
TSM integrates concentration data and meteorological transport information.
1
Measure PM / species
2
Calculate back trajectories
3
Join by arrival time
4
Grid endpoints
5
Compute CPF/PSCF or CWT
Output maps do not identify exact emission points. They identify geographic regions and pathways statistically associated with elevated receptor concentrations.
07

## Slide 8
Method family: what each map answers
Use multiple views together to avoid over-interpreting any single method.
Frequency
Where did air masses pass most often?
Cluster analysis
Which air-mass pathways are similar?
CPF / PSCF
Where did trajectories pass during high events?
CWT
Where are trajectories associated with higher concentrations?
This presentation emphasizes CPF/PSCF and CWT because they connect measured concentrations to trajectory residence time.
08

## Slide 9
CPF / PSCF: the probability view
CPF asks: when concentrations are high, where did the air masses pass?
All trajectory endpoints in cell
Endpoints during high PM events
CPF / PSCF probability
For each grid cell: count all endpoints and count endpoints linked to high concentrations.
High value = the cell is frequently crossed before high concentration days.
In openair trajectory analysis this is implemented as statistic = "pscf".
09

## Slide 10
CPF / PSCF formula and interpretation
A simple ratio: high-event residence divided by all residence.
CPFᵢⱼ / PSCFᵢⱼ = mᵢⱼ / nᵢⱼ
nᵢⱼ = all trajectory endpoints in grid cell (i,j)
mᵢⱼ = endpoints in cell (i,j) when concentration is high
high = often >90th percentile
(adjust with percentile option)
• Best for identifying regions linked to high-concentration episodes.
• Cells with few endpoints should be down-weighted or excluded.
• CPF/PSCF is a probability map, not a concentration map.
10

## Slide 11
CWT: the concentration-weighted view
CWT asks: what average receptor concentration is associated with air passing over each grid cell?
Trajectory endpoints carry the arrival concentration
Grid cells accumulate concentration-weighted residence time
High CWT = cell linked to higher receptor concentrations
Each cell receives a weighted value based on the pollutant concentration measured when those trajectories arrived.
In openair: trajLevel(..., statistic = "cwt")
11

## Slide 12
CWT formula and interpretation
CWT preserves concentration intensity, unlike CPF/PSCF threshold counting.
CWTᵢⱼ = Σ(Cₖ τᵢⱼₖ) / Σ(τᵢⱼₖ)
Cₖ = pollutant concentration at arrival of trajectory k
τᵢⱼₖ = residence time of trajectory k in cell (i,j)
High CWT value
Air parcels passing this cell are, on average, associated with high receptor concentrations.
Important
CWT is useful for ranking potential source regions, but must still be interpreted with emissions, meteorology and chemical tracers.
12

## Slide 13
CPF/PSCF versus CWT
They answer related but different questions. Use both when possible.
Feature
CPF / PSCF
CWT
Core question
Where were trajectories during high events?
Which cells are linked to higher average concentrations?
Output
Probability / conditional probability
Concentration-weighted field
Strength
Highlights high-event pathways
Preserves concentration intensity
Main caution
Threshold choice matters
Hot cells can reflect trajectory frequency and outliers
Teaching shortcut: CPF/PSCF says “how often during high events”; CWT says “how high on average”.
13

## Slide 14
Practical choices before mapping
Method settings influence the maps. Sensitivity tests are part of the analysis.
Trajectory length
72–120 h common for regional PM
Starting height
test near-surface and elevated arrivals
Grid size
coarse enough for sufficient endpoints
High threshold
often 90th percentile for CPF/PSCF
Minimum bin
remove or down-weight sparse cells
Smoothing
helps visualization but can blur details
Always report key settings: meteorology, receptor height, trajectory duration, grid increment, percentile, min.bin and smoothing.
14

## Slide 15
Interpretation rules
Trajectory maps suggest regions and pathways — they do not prove emission sources alone.
Do
• use many trajectories
• compare CPF/PSCF and CWT
• check chemical tracers
• test seasons and heights
• cross-check with emissions and events
Do not
• interpret one trajectory as proof
• ignore local sources
• over-read sparse grid cells
• forget trajectory uncertainty
• hide sensitivity choices
Best practice: combine trajectory maps with meteorology, source apportionment, satellite products, emission inventories and known events.
15

## Slide 16
Part II
Practical workflow
HYSPLIT + openair
Install tools, prepare trajectories, run CPF/PSCF and CWT examples.
1. Generate trajectories
2. Import to R
3. Map CPF/CWT
16

## Slide 17
The software toolchain
HYSPLIT generates air-mass trajectories; openair analyses and maps them with air-pollution data.
HYSPLIT
trajectory model
Trajectory endpoint table
date • lat • lon • hour.inc
openair in R
trajPlot • trajLevel • trajCluster
PM / species time series
joined by arrival time
Minimum data idea: every trajectory endpoint inherits the pollutant concentration measured when the air mass arrived at the receptor.
17

## Slide 18
Install R, RStudio and openair
openair is installed from CRAN and used inside R or RStudio.
1
Install R
2
Install RStudio
(optional but recommended)
3
Install packages
4
Load libraries
install.packages("openair")
install.packages(c("tidyverse", "lubridate"))
library(openair)
library(tidyverse)
library(lubridate)
Tip: after loading openair, use ?openair or ?trajLevel for function documentation.
18

## Slide 19
openair data requirements
Correct column names and date formatting prevent most problems.
Air-quality data
Trajectory data
Joined dataset
• date column in POSIXct format
• pollutants as numeric columns
• ws and wd for local wind analyses
• date = arrival time
• date2 = endpoint time
• lat, lon, height, hour.inc
• merge by date
• each endpoint carries arrival concentration
• ready for trajPlot and trajLevel
Column names are case-sensitive: use date, lat, lon, hour.inc, ws and wd where relevant.
19

## Slide 20
HYSPLIT: two ways to work
Use the web version for quick runs, or install locally for repeated / scripted analyses.
READY web version
• no local install
• good for teaching and small numbers of trajectories
• manual setup through web forms
Desktop / local HYSPLIT
• Windows, Mac and Linux options
• GUI and script workflows
• better for batch trajectory production
For training: start with READY web trajectories, then move to local HYSPLIT when the analysis requires many receptor times, heights or sites.
20

## Slide 21
Part IIa
Installing
HYSPLIT
locally
A Windows-focused procedure for trajectory calculation and openair workflows.
HYSPLIT installation workflow
No screenshots: procedure only. Use the READY web version for quick demonstrations; install locally for batch work.
20
1 Utilities
Install Tcl/Tk + graphics tools first
2 HYSPLIT
Download and install the model
3 Configure
Check GUI paths and shortcut
4 Test
Run one backward trajectory
Install to a simple folder such as C:\hysplit and avoid spaces in paths.
The public/unregistered version is sufficient for trajectory calculations.
Verify that the GUI opens and that a sample trajectory runs before producing many trajectories.
Source: uploaded HYSPLIT installation PDF and NOAA ARL Windows installation guidance.

## Slide 22
Install locally or use READY web?
Choose the simplest workflow that matches the task.
21
READY web version
Local desktop installation
No local model installation.
Good for teaching and single trajectories.
Useful when only a few receptor times are needed.
Less convenient for large batches or automated workflows.
Runs through GUI or scripts.
Better for repeated analyses, many dates, multiple heights or sites.
Requires utilities and correct path configuration.
Recommended for reproducible research workflows.
Teaching sequence: demonstrate with READY → install locally → automate batch trajectories.

## Slide 23
Step 1 — choose the HYSPLIT download
For this course, the public/unregistered version is enough for trajectory exercises.
22
Public / unregistered
version
Use this for computing archive or forecast back trajectories. It is suitable for CPF/PSCF, CWT and clustering exercises because those methods only need trajectory endpoints.
Registered
version
Registration mainly affects some dispersion/concentration calculations with forecast meteorology. It is not required for the trajectory-only workflow used in this presentation.
Install path recommendation: C:\hysplit — avoid folders with spaces, such as “Program Files”.
Note: older HYSPLIT4 tutorials may refer to C:\hysplit4; use the path that matches your installation and update examples accordingly.

## Slide 24
Step 2 — install required utilities first
The HYSPLIT model can run from command line, but the GUI and graphics need supporting tools.
23
Tcl/Tk
Required to run the HYSPLIT graphical user interface. If using ARL tcl.zip, unzip it for example to C:\tcl.
Ghostscript
Used for viewing/printing PostScript graphics generated by HYSPLIT plotting programs.
GSView
Legacy PostScript viewer. It may be useful for older workflows, but it is no longer actively supported.
ImageMagick
Used to convert PostScript graphics. During installation, enable legacy utilities when prompted.
Recommended order: Tcl/Tk → Ghostscript / GSView → ImageMagick → HYSPLIT
If utilities are already installed from a previous HYSPLIT version, they usually do not need to be reinstalled.
Administrator rights may be required, especially on institutional computers.

## Slide 25
Step 3 — install HYSPLIT on Windows
After utilities are installed, install the model itself.
24
1
Open the NOAA ARL HYSPLIT download page
Use the official READY / HYSPLIT pages and select the Windows PC version.
2
Read the use agreement
The download page requires confirmation of the HYSPLIT use agreement.
3
Enter your email and agree
Provide an email address if requested, then proceed to the download link.
4
Run the installer
Use the 64-bit Windows installer or unzip the distribution according to the NOAA instructions.
5
Choose a simple folder
Install to C:\hysplit or another path without spaces. Keep the location consistent for scripts and examples.
Before moving to openair: confirm that HYSPLIT can produce one trajectory endpoint output file.

## Slide 26
Step 4 — configure the shortcut and test the GUI
This is mainly needed when Tcl/Tk was installed separately or from the ARL zip file.
25
Check the desktop shortcut target. The Tcl/Tk interpreter should call the HYSPLIT GUI script.
C:\tcl\bin\wish86t.exe C:\hysplit\guicode\hysplit.tcl
Right-click “Run Hysplit” and open Properties.
In Target, place the Tcl/Tk interpreter before the HYSPLIT Tcl script.
Separate the two paths with one blank space.
Use the correct folder names for your installation.
Open the GUI.
Run one simple backward trajectory.
Check that a plot and endpoint file are created.
Only then proceed to batch trajectory production.
Older installations may use C:\hysplit4\guicode\hysplit4.tcl — always match the command to your installed folder.

## Slide 27
HYSPLIT installation: checklist and troubleshooting
Most problems come from paths, permissions, utilities, or missing meteorological data.
26
Path problems
• Avoid spaces in folder names
• Use C:\hysplit or similar
• Check shortcut target carefully
Utility problems
• Tcl/Tk needed for GUI
• Ghostscript/GSView for PostScript
• ImageMagick for conversion
Permission problems
• Install as administrator if needed
• Ask IT for managed computers
• Check antivirus/quarantine rules
Run problems
• Confirm meteorological data exist
• Test one trajectory first
• Check UTC times and heights
Course checkpoint: produce one backward trajectory, save the endpoint table, then import it into R/openair.
For class exercises, document: HYSPLIT version, install path, meteorological dataset, receptor coordinates, heights, duration, and UTC arrival times.

## Slide 28
Running a HYSPLIT trajectory
The same basic settings appear in the web and desktop interfaces.
Direction
Backward for source-region analysis
Meteorology
choose archive or forecast data
Start time
match sample / measurement time
Location
receptor latitude and longitude
Height
e.g. 100, 500, 1000 m AGL
Duration
e.g. 72 or 96 h back
Export or save the trajectory endpoints; openair needs the endpoint coordinates and the trajectory arrival date.
21

## Slide 29
From HYSPLIT output to openair input
The key step is converting trajectory output into a tidy endpoint table.
HYSPLIT output file
Clean / reshape endpoints
Join PM data by date
Plot and grid in openair
traj <- read.csv("hysplit_openair.csv") |>
mutate(date = ymd_hms(date, tz = "UTC"),
date2 = ymd_hms(date2, tz = "UTC"))
pm <- read.csv("pm_data.csv") |>
mutate(date = ymd_hms(date, tz = "UTC"))
traj_pm <- left_join(traj, pm, by = "date")
22

## Slide 30
Example 1: import and plot trajectories
openair can import pre-calculated HYSPLIT trajectories for supported sites.
library(openair)
library(tidyverse)
traj <- importTraj(site = "london", year = 2010)
# quick check
head(traj)
# plot all trajectories
trajPlot(traj)
What to look for
• arrival date and endpoint date
• trajectory duration
• main transport sectors
• height evolution
Use trajPlot() first to understand the raw trajectories before calculating statistics.
23

## Slide 31
Example 2: link trajectories to pollutant data
Trajectory analysis becomes powerful when each endpoint is linked to measured concentration.
# Example with UK monitoring data
kc1 <- importUKAQ("kc1", year = 2010)
traj_pm <- left_join(traj, kc1, by = "date")
# plot trajectories coloured by PM10
trajPlot(traj_pm, pollutant = "pm10",
cols = "turbo", lwd = 1)
Interpret carefully
• high PM on a trajectory can still be local
• check NOx, local winds and time series
• compare rural/background sites when possible
For PM components with regional character, such as sulfate, nitrate, PM2.5 and dust tracers, trajectory methods are usually more informative.
24

## Slide 32
Example 3: CPF / PSCF map in openair
Use trajLevel() with statistic = "pscf".
traj_pm |>
filter(lon > -20, lon < 20, lat > 45, lat < 60) |>
trajLevel(
pollutant = "pm2.5",
statistic = "pscf",
percentile = 90,
min.bin = 10,
cols = "increment",
border = NA
)
Read the map as:
• probability map
• high-event pathways
• sensitive to percentile
• low-count cells need caution
Shortcut: CPF/PSCF = “where trajectories passed before high PM events”.
25

## Slide 33
Example 4: CWT map in openair
Use trajLevel() with statistic = "cwt".
traj_pm |>
filter(lon > -20, lon < 20, lat > 45, lat < 60) |>
trajLevel(
pollutant = "pm2.5",
statistic = "cwt",
smooth = TRUE,
cols = "increment",
border = "white"
)
Read the map as:
• concentration-weighted field
• hotspots linked to high average PM
• good complement to CPF/PSCF
• check outliers and smoothing
Shortcut: CWT = “how high PM tends to be when air passes over this region”.
26

## Slide 34
Example 5: seasonal and sensitivity checks
Split the analysis and test whether the interpretation is stable.
# seasonal CPF/PSCF panels
trajLevel(traj_pm, pollutant = "pm2.5",
statistic = "pscf", type = "season",
percentile = 90, ncol = 4)
# change grid resolution
trajLevel(traj_pm, pollutant = "pm2.5",
statistic = "cwt",
lon.inc = 2, lat.inc = 2)
# cluster pathways
clust <- trajCluster(traj_pm, method = "Angle", n.cluster = 6)
Sensitivity checklist
• percentile
• grid size
• trajectory height
• trajectory duration
• season / event period
• min.bin / weighting
27

## Slide 35
Practical exercise: from trajectories to maps
A suggested hands-on activity for students.
A
Plot trajectories for an event period
B
Colour trajectories by PM10 or PM2.5
C
Create a CPF/PSCF map using the 90th percentile
D
Create a CWT map and compare with CPF/PSCF
E
Repeat by season or with a different grid size
Deliverable: one slide with the event trajectory plot, one CPF/PSCF map, one CWT map, and three bullet points on interpretation and uncertainty.
28

## Slide 36
Take-home messages
The best trajectory analysis is statistical, reproducible and cautious.
• Long-range transport can strongly influence PM and its chemical components.
• Back trajectories estimate air-mass history; use large ensembles and statistical maps.
• CPF/PSCF highlights regions crossed before high-concentration events.
• CWT highlights regions associated with higher average receptor concentrations.
• HYSPLIT provides trajectories; openair provides plotting and trajectory-statistical tools.
• Interpret maps together with chemistry, meteorology, local emissions and sensitivity tests.
Core principle: maps suggest potential source regions and transport pathways, not proof of source emissions alone.
29

## Slide 37
Selected sources and further reading
Core sources used for this teaching deck.
• Openair book: Introduction, openair package, trajectory analysis, and HYSPLIT trajectory files.
• NOAA ARL HYSPLIT / READY documentation and installation pages.
• Uploaded “R Practical Exercise” teaching material.
• Fleming et al. (2012), Seibert et al. (1994), Lupu & Maenhaut (2002), Hsu et al. (2003), Stein et al. (2015).
Recommended final step for students: reproduce one CPF/PSCF and one CWT map with their own PM component time series.
30